## Slide 1: Memory

## Slide 2: Memory
The memory is that part of the computer where programs and data are stored
Memories consist of a number of cells (or locations), each of which can store a piece of information
Each cell has a number, called its address, by which programs can refer to it
If a memory has n cells, they will have addresses 0 to n − 1
All cells in a memory contain the same number of bits

## Slide 3: Memory Example

## Slide 4: Use of Various Technologies

## Slide 5: Technologies used in Memory Design
Types of memories
  Random Access Memory (RAM): Memory from where data can be read and where data can be written – Volatile
    Static RAM (SRAM)
    Dynamic RAM (DRAM)
  Read Only Memory (ROM): Memory from where data can be read, but not where data can be written
    Useful for booting up, fixed data

## Slide 6: Static RAM (SRAM)
Static RAM (SRAM) is constructed using flip-flops
Very fast - Access time is a nanosecond or less, so popular as cache memory
Consume more power
Volatile storage (no power, no storage)

## Slide 7: Dynamic RAM (DRAM)
Dynamic RAM (DRAM) uses capacitors to store data
Requires periodic refreshing, unlike SRAM
Low cost, high capacity; so suitable as main memory (RAM)
Volatile storage (no power, no storage)

## Slide 8: ROM
The data in a Read Only Memory (ROM) is inserted during its manufacture
The only way to change the program in a ROM is to replace the entire chip
Much cheaper than RAM
PROM (Programmable ROM) allows companies to write to the ROM chip once, not at the time of chip manufacturing
  Example: A washing machine manufacturer can buy ROM chips and write its instructions on the chip

## Slide 9: Auxiliary Storage
Auxiliary storage, also known as secondary memory or external storage, refers to the non-volatile storage devices that retain information even when the power supply is disconnected
Examples: HDD, SSD, Flash memory, Optical storage

## Slide 10: Hard Disk Drive (HDD)
Mechanical storage devices
Use magnetic material to store data
High capacity, low cost
These days replaced by SSD

## Slide 11: Flash Memory
Non-volatile memory
Retains data even when there is no power supply
Used in Solid State Drives (SSD), USB drives, memory cards
Low power consumption and durable
Other varieties: NAND flash memory or NOR flash memory

## Slide 12: Solid State Drive (SSD)
Use NAND flash memory
Faster, more durable

## Slide 13: Optical Storage
CD-ROM, DVD, Bluray disks
Magnetic disk contains information
Used more for music, movies, etc

## Slide 14: Cache Memory

## Slide 15: Cache Memory
Two-level cache

## Slide 16: Cache Memory
CPU registers are limited in number (cost, CPU chip size are key factors)
More small, fast memory called cache memory is used (cacher: to hide in French, and pronounced ‘cash’)
The most heavily used memory words are copied in the cache – CPU first checks cache, if data is not in cache, it goes to main memory

## Slide 17: Principle of Locality
A program accesses a relatively small portion of address space at any given time
Two types of principle of locality
  Temporal locality (Locality in time): If some data is referenced, it will be referenced again soon
  Spatial locality (Locality in space): If some data is referenced, data near it will also be referenced

## Slide 18: Example
sum = 0;
for (i = 0; i < n; i++)
  sum += a[i];
return sum;
Data
  Temporal: Variable sum is referenced in each iteration
  Spatial: array a[] is accessed
Instructions
  Temporal: Cycle through the loop repeatedly
  Spatial: Reference instructions in sequence

## Slide 19: Hit Ratio, Miss Ratio
Hit Ratio (%) = (Number of Cache Hits / Total Memory Accesses) × 100%
Miss Ratio = 100% - Hit Ratio
Example: Suppose you have a cache system in a web server that receives 1,000 requests for web pages, and the cache is able to serve 800 of those requests from the cache (cache hits), while the remaining 200 requests had to be fetched from the main server (cache misses)
Hit Ratio = (800/1000) x 100 = 80% and Miss Ratio = 100% - 80% = 20%

## Slide 20: Cache Optimizing Techniques
Cache size optimization: Increase cache size (but cost will increase)
Cache replacement policies: Least Recently Used (LRU), Most Recently Used (MRU), Random
Cache associativity: Mapping of cache lines to cache sets (Discussed separately)
Prefetching: Cache anticipates and fetches data before it is actually demanded
Write policies: Write-back (Write only in cache and update main memory only when necessary) or Write-through (Write to cache and to main memory)
Data locality: Repeated access to same instructions/data
Multi-level cache: L1 (Fastest) to L3 (Slowest) – See next slide

## Slide 21: Cache Concept

## Slide 22: Cache Associativity
Direct-mapped cache: One memory location -> One cache location
Set-associative cache: Deals with cache conflict
Fully associative cache: No mapping between memory location and cache location, any memory block can be stored anywhere in cache (Not discussed here)

## Slide 23: Direct-Mapped Cache
Consider 16-bit memory addresses, 128 cache lines, and 32-byte cache blocks
A memory address is divided into three parts:
  Tag: Identifies memory blocks’ location in the main memory
  Index: Which set/slot in cache is used for which memory block?
  Offset: Identifies a specific byte in cache
Example: Suppose our program now wants to read from memory location 1010000001100100

## Slide 24: Direct-Mapped Cache
Example: Suppose our program now wants to read from memory location 1010000001100100 and cache is blank
This index binary value 0000011 i.e. 3 in decimal is used to lookup the cache

## Slide 25: Direct-Mapped Cache
Since the cache line was empty, this was a cache miss. We need to go to main memory location 1010, get the 32-byte block from there, write in the cache at index 00000011, update the valid flag to 1 and return the 32-bit block to the program. Next time whenever anyone wants to read the 32-byte block at memory location 1010, we will have a cache hit.

## Slide 26: Set-Associative Cache
Direct-mapped cache can cause cache conflict
Example: Suppose cache has 4 slots/sets (indexed with 2 bits) and main memory has 16 blocks (indexed with 4 bits)
With 2 bits for indexing, cache sets are 00, 01, 10, 11
But main memory has 16 blocks from 0000 to 1111
Result:
  Memory block 0000 and memory block 0100 both map to set 00 in the cache
  Memory block 0001 and memory block 0101 both map to set 01 in the cache
  Memory block 0010 and memory block 0110 both map to set 10 in the cache
  Memory block 0011 and memory block 0111 both map to set 11 in the cache
Which is correct, in each of the four cases? Solution: Set-associative cache

## Slide 27: Set-Associative Cache: Both are Correct!
Memory block 0000 and memory block 0100 both map to set 00 in the cache
Memory block 0001 and memory block 0101 both map to set 01 in the cache
Memory block 0010 and memory block 0110 both map to set 10 in the cache
Memory block 0011 and memory block 0111 both map to set 11 in the cache
We now create two entries per cache set/slot to map both addresses
LRU | V0 | D0 | Tag | Data | V1 | D1 | Tag | Data
0/1 |  |  | 0000 |  |  |  | 0100 | 
0/1 |  |  | 0001 |  |  |  | 0101 | 
0/1 |  |  | 0010 |  |  |  | 0110 | 
0/1 |  |  | 0011 |  |  |  | 0111 | 
Cache set
00
01
10
11

## Slide 28: Set-Associative Cache
Suppose our program now wants to read from memory block 0000
This will map to cache set 00 (but the first half), so if the valid bit is set, data will be read from there; else from actual memory block 0000, causing a cache miss
Next, suppose our program now wants to read from memory location 0100
Even this will map to cache set 00 (but the second half), so if the valid bit is set, data will be read from there; else from actual memory block 0100, causing a cache miss

## Slide 29: Cache Coherence
In a multiprocessor/multicore system, multiple processors can access and modify shared data in the main memory
Each processor has its own cache for faster access
When one processor writes to a memory location, other processors might still have a copy of that data in their caches - This situation can lead to inconsistencies and data corruption if not managed properly
Cache coherence ensures the consistency and integrity of data stored in multiple caches in a multiprocessor or multicore system
Cache coherence protocols: MESI, MOESI, Write-through/Write-behind

## Slide 30: MESI
MESI (Modified, Exclusive, Shared, and Invalid)
Tracks the state of each cache line (block) in a cache
When a processor modifies a cache line, it marks it as "Modified" and ensures that other caches invalidate their copies
When a cache line is read but not modified, it can be marked as "Shared" or "Exclusive" depending on whether other caches have copies

## Slide 31: MOESI
MESI (Modified, Owner, Exclusive, Shared, and Invalid)
Same as before, with an addition
The "Owner" state is used to identify which cache has the exclusive right to modify a cache line
When a cache line is in the "Owner" state, other caches can read it but cannot modify it

## Slide 32: Write-Through/Write-Behind Caches
Write-through caches: All writes are immediately written to main memory, ensuring that all processors see the updated data promptly
Write-behind caches: Delay writing updates to main memory, which can introduce complexities in maintaining coherence

## Slide 33: Mechanisms to Enforce Cache Coherence Protocols
Invalidation: When one processor writes to a memory location, it sends an invalidation signal to other caches holding copies of that data, forcing them to invalidate their copies
Broadcast: Some protocols use broadcast messages to inform other caches of updates, ensuring that all caches are aware of changes to shared data
Snooping: Caches "snoop" or monitor memory transactions on the memory bus to detect and respond to changes in shared data

## Slide 34: Using a Finite-State Machine to Control a Simple Cache
Using a Finite State Machine (FSM) to control a simple cache involves designing a set of states and transitions that manage cache operations
A cache FSM typically handles read and write operations, cache coherence, cache line replacement, and other control tasks
Defines states, inputs (events) and outputs (actions) using transition logic
States: Idle, Read, Write, Cache miss, Cache coherence
Inputs: External commands that change the state – Read, Write, Cache miss signal, Cache coherence signal
Outputs: Read requests to main memory, Updating of cache lines, Notifying the CPU of cache hits/misses, etc
Transition logic: Conditions under which state transitions can occur (Example: When a Read request is received, state might change from idle to read)

## Slide 35: Sample FSM for Cache Operations

## Slide 36: AMD Zen Memory and Intel Skylake Memory Hierarchy
L1 cache
L2 cache
L3 cache (Last cache)
Main memory (DRAM)

## Slide 37: Memory Interleaving
Memory interleaving is a technique to improve memory access performance by distributing data across multiple memory modules or banks
Breaks up memory into smaller segments, or "interleaves," and distributes data evenly among them
For example, if we have two memory modules, the memory space might be divided into two interleaves: Interleave 0 and Interleave 1
When data is written to or read from memory, it is distributed across the interleaves in a round-robin fashion: For instance, the first data word goes to Interleave 0, the second to Interleave 1, the third to Interleave 0 again, and so on
Allows for parallel memory access because multiple interleaves or banks can be accessed simultaneously
More useful in multi-core processors where multiple processors may need to access memory concurrently

## Slide 38: Memory Interleaving Example
Suppose we decide to use 4 interleaved memory modules
  Module 0 will contain memory addresses 0, 4, 8, 12, 16, …
  Module 1 will contain memory addresses 1, 5, 9, 13, 17, …
  Module 2 will contain memory addresses 2, 6, 10, 14, 18, …
  Module 3 will contain memory addresses 3, 7, 11, 15, 19, …
Advantage: The CPU(s) can read memory modules one after the other quickly to access data. For example, suppose an instruction needs data from memory locations 2 to 9. The CPU can quickly go to memory module 2, then to 3, then to 1, then to 2 again, etc.

## Slide 39: Virtual memory – The need
Consider a computer that has actual physical memory of 4096 (212) words, but 65536 (216) memory addresses
Real memory locations: Addressable memory locations:
Binary | Decimal
000000000000 | 0
000000000001 | 1
000000000010 | 2
… | …
111111111111 | 4095
Binary | Decimal
0000000000000000 | 0
0000000000000001 | 1
0000000000000010 | 2
… | …
0000111111111111 | 4095
… | …
… | …
1111111111111111 | 65535

## Slide 40: Explanation
Suppose we have a 16-bit computer
This means that the computer has 16 wires between the CPU and the main memory of the computer, i.e. Address bus is of 16 bits
So, the actual addressable addresses (216) are 65,536
But suppose the main memory only has 4096 memory locations
Result: Memory addresses from 4096 to 65,535 are useless for us
See next slide

## Slide 41: Main Memory and Addressable Memory
Memory address 4095
Memory address 4094
…
…
…
Memory address 0
Memory address 65535
Memory address 65534
…
…
Memory address 4095
Memory address 0
Unusable addresses
Physical memory
Addressable memory

## Slide 42: Virtual Memory Concept – Use of Secondary Storage

## Slide 43: Virtual Memory – Benefits
In our example, a programmer can write a program, which assumes that there are 65,536 locations in the main memory, and not just 4096
In other words, the programmer can utilize the full 16-bit address space, when in reality there are only 4096 real memory locations
At a time, 4096 memory words would be loaded from virtual memory (i.e. secondary storage) into physical memory
If the program needs a word outside of these currently loaded words, a page fault occurs
The operating system will remove the current 4096 words from the physical memory and replace them with the needed words

## Slide 44: Page Replacement algorithms to Handle Page Faults
Least Recently Used (LRU) algorithm: Evicts the page least recently used because of the probability of its not being in the current working set is high
First In First Out (FIFO): Removes the least recently loaded page, independent of when this page was last referenced. Associated with each page frame is a counter. Initially, all the counters are set to 0. After each page fault has been handled, the counter for each page presently in memory is increased by one, and the counter for the page just brought in is set to 0. When it becomes necessary to choose a page to remove, the page whose counter is highest is chosen.

## Slide 45: Terminology
The addresses that the program can refer to are in the virtual address space, and the actual, hardwired (physical) memory locations are in the physical address space
A memory map or page table specifies for each virtual address what the corresponding physical address is
For this, both the virtual memory and physical memory is divided into equal-sized pages

## Slide 46: Divide Virtual Memory into Pages and Physical Memory into Page Frames
Virtual memory
Physical memory

## Slide 47: Thrashing concept
A program that generates page faults frequently and continuously is said to be thrashing
Needless to say, thrashing is an undesirable characteristic

## Slide 48: Associative Memory
Associative memory, often called as Content-Addressable Memory (CAM) or associative storage, is a type of computer memory that allows data to be retrieved based on its content rather than its specific memory address
Tags/keys are identified for search keywords/patterns and stored with the data
We search for content or pattern, instead of providing memory address
Parallel search is possible, leading to high performance
No need to sequentially look up memory addresses, so fast
Used in cache memory, network routers and applications where fast search is needed

## Slide 49: An Overview of Latest Processors

## Slide 50: Intel 32-bit and 64-bit Processors
Point | 32-bit processor | 64-bit processor
Architecture | X86 family, works with data and instructions that are 32-bit long | X86-64 or AMD64 family, works with data and instructions that are 64-bit long
Memory addressing | 2^32 i.e. 4GB memory addresses can be accessed | 2^64 i.e. 18.4 million TB memory addresses can be accessed
Software compatibility | Compatible with 32-bit and 16-bit software | Compatible with 64-bit and 32-bit software
Performance | Struggle with memory-intensive applications | Suitable for memory-intensive applications using multi-core
Limitations | 4GB RAM, Handling large data sets is slow | None at the moment

## Slide 51: Generations of Intel Core Processors
Generation | Year | Brand names
First (Nehalem) | 2008 | Core i7, Core i5, Core i3
Second (Sandy Bridge) | 2011 | Intel Quick Sync Video
Third (Ivy Bridge) | 2012 | -
Fourth (Haswell) | 2013 | -
Fifth (Broadwell) | 2014 | -
Sixth (Skylake) | 2015 | -
Seventh (Kaby Lake) | 2016 | -
Eighth (Coffee Lake) | 2017 | More cores and threads in existing processors
Ninth (Coffee Lake Refresh) | 2018 | -
Tenth (Comet Lake and Ice Lake) | 2019 | -
Eleventh (Tiger Lake) | 2020 | -

## Slide 52: HPC Processors: AMD, POWER, ARM
AMD, with its x86-based processors, has a significant presence in HPC, particularly in the consumer and mid-range server segments
AMD's EPYC processors have gained popularity in HPC clusters due to their competitive performance, memory bandwidth, and core counts
Key features include support for PCIe 4.0 for high-speed I/O and excellent floating-point performance
AMD's Infinity Fabric interconnect architecture allows for scalable multi-socket systems, making it suitable for a variety of HPC workloads
AMD's partnership with Cray (now part of HPE) has resulted in the development of powerful supercomputers like "Frontier" and "El Capitan"

## Slide 53: HPC Processors: AMD, POWER, ARM
IBM POWER architecture is known for its high-performance computing capabilities and is used in some of the world's most powerful supercomputers
POWER processors are characterized by high core counts, significant memory bandwidth, and advanced vector processing units
IBM's Summit supercomputer, located at Oak Ridge National Laboratory, is one of the most prominent examples of POWER-based HPC systems - It was, at one point, the world's fastest supercomputer
IBM's involvement in the OpenPOWER Consortium has led to the availability of open-source hardware designs and increased adoption of POWER-based systems in HPC

## Slide 54: HPC Processors: AMD, POWER, ARM
ARM processors, initially designed for mobile devices, are gaining traction in HPC due to their power efficiency and scalability
ARM-based processors, such as those from vendors like Cavium (now Marvell) and Fujitsu, are being used in HPC systems
ARM's approach to heterogeneous computing, with big.LITTLE configurations and accelerators, is well-suited for workloads that require both high performance and energy efficiency
ARM processors are often used in conjunction with GPUs or accelerators, allowing for balanced HPC systems
The ARM ecosystem's flexibility enables customized processor designs for specific HPC applications and research needs
Notable HPC Systems:
The "Fugaku" supercomputer, developed by RIKEN and Fujitsu, is currently the world's fastest supercomputer and is powered by ARM-based processors
Other ARM-based HPC systems, like the "Astra" supercomputer at Sandia National Laboratories, demonstrate the architecture's viability in the HPC space