## Slide 1: Storing Floating Point Numbers in Computer Memory
A floating point number is stored in memory as made up of three parts:
  Sign
  Exponent
  Significant value

## Slide 2: Storing Floating Point Numbers in Memory – Step 1: Significant Part
We need to convert the number into the normalized form
For floating point numbers, we need to normalize it as:
1.significant bit * 2 exponent
Decimal 10.75 = Binary 1010.11
So, 1010.11 will be normalized as: 1.01011 * 23
Because, after the first 1, we write the decimal
point and then write the remaining digits
of the original number (i.e. 01011)
Significant part is 1.01011 in binary

## Slide 3: Storing Floating Point Numbers in Memory – Step 2: Calculate Exponent
We do not use 2’s complement for floating point numbers
We need to add bias to the exponent, regardless of whether the number is positive or negative
biasn = 2n-1 – 1 … Note n = Number of bits used for exponent
bias8 = 28 - 1 -1 = 127
Hence the normalized exponent value will be:
Actual exponent = Exponent + bias value which is 3 + 127 = 130
So, the final exponent is 130
Binary form of 130 is 100000102

## Slide 4: Storing Floating Point Numbers in Memory – Summary
Sign bit = 0, because 10.75 is positive
Exponent = 130, which is 10000010
Significant value is 1.01011, here we eliminate 1 before the dot (.) and just take the part after the dot, i.e. only 01011

## Slide 5: Storing Floating Point Numbers in Memory – End Result

## Slide 6: Half Adder
Half adder is a logic circuit that adds 2 bits
It produces two outputs: sum and carry
Sum = 1 when A and B are different (XOR gate)
Carry = 1 when A and B are 1 (AND gate)
XOR

## Slide 7: Full Adder
Full adder is a logic circuit that can add 3 bits
XOR is true when we have ODD number of 1s

## Slide 8: Flip-flop
Gates are useful for decision-making – they can be used to perform addition and subtraction
Decision-making elements are not enough – a computer also needs memory elements to store bits
Flip-flops are used for memory elements
A flip-flop is a device with two stable states and it retains one of these two states until triggered into the other
A flip flop can store one bit of data

## Slide 9: Creating a 1-Bit Computer Memory (i = Input, s = switch/trigger)
2
i
s
1
3
4
a
b
c
o

## Slide 10: Understanding How It Works; s = 1 and i = 0 (Other combinations not described)
Suppose s = 1, i = 0
Since i and s go into gate 1, we have a = (1 NAND 0) = 1
Since a and s go into gate 2, we have b = (1 NAND 1) = 0
Since b is 0, which goes into gate 4, gate 4’s output: c = 1
Since c = 1 and a = 1, output of gate 3: o = (1 NAND 1) = 0
Now o, which is 0, goes back to gate 4 as the second input, once again c = (0 NAND 0) = 1
So, with s = 1, o = i = 0 and the 0 bit of input is retained as 0 in the output
i
s
1
3
4
a
b
c
o
2

## Slide 11: Computer History

## Slide 12: Computer Organization and Architecture
Computer organization: Physical aspects of a computer system (e.g. circuit design, control signals, memory types)
Computer architecture: Logical aspects of a computer as seen by a programmer (e.g. instruction sets, instruction formats, data types)

## Slide 13: Organization Architecture
Also called microarchitecture or low level architecture
Transparent to the programmer (e.g. a programmer does not need to know how an addition operation is performed by the hardware)
Deals with physical components
How to do (Implementation)
High-level architecture
Programmer has to be aware of the instructions that are used
Deals with logical components (instruction set, addressing mode, data types)
What to do (Instruction set)

## Slide 14: Brief History of Computers
Generation | Time Period | Details
0th (Mechanical computers) | 1642-1945 | Mechanical devices (e.g. Difference Engine and Analytical Engine of Charles Babbage) – See next slide Konrad Zuse’s calculating machines using electric relays John Atanasoff’s calculator
1st (Vacuum tubes) | 1945-1955 | COLOSSUS in England (Alan Turing), ENIAC (Mauchley and Eckert)
2nd (Transistors) | 1955-1965 | Digital Equipment Corporation (DEC) PDP-1, CDC 6600, Cray Supercomputers
3rd (Integrated Circuits or ICs) | 1965-1980 | IBM System/360 series of computers – Same assembly language, multiple computers, introduced multiprogramming,
4th (Very Large Scale Integration or VLSI) | 1980-Ongoing | IBM and other ‘cloned’ Personal Computers (PC), Apple Macintosh, CP/M and DOS operating systems, Intel 80836 chip in 1985 (x86)
5th (Low power and invisible computers) | 1990s onwards | PDAs, Smart phones, IoT

## Slide 15: Computer Performance – Moore’s Law

## Slide 16: The Intel CPU Family

## Slide 17: The von Neumann Architecture

## Slide 18: The ‘Bus’ Concept

## Slide 19: Computer Bus
The computer bus is a communication link (set of wires) used inside a computer to send data, addresses, control signals, and power to various hardware components
Buses connect various hardware components to each other
Bus types
  Address bus: Connects CPU to RAM, used for specifying memory addresses for reading or writing of data
  Data bus: Connects CPU to RAM, specifies data to be written or contains data that was read
  Control bus: Connects CPU to RAM for passing control signals
Address bus + Data bus + Control bus = System bus